## Slide 1: Moving Past the Arduino IDE for Embedded Development

## Slide 2: Abstract
Learn how to write embedded software with tools that aren’t the Arduino IDE
Learn how to work with C/C++ for embedded development

## Slide 3: Speaker Bio
Al Rodriguez
.NET Dev for over a decade
Java Dev for the beginning of that
@ProgrammerAL on Twitter

## Slide 4: Steps to Create an Embedded App
1) Type out the code
2) Compile to Native Instructions (8-bit ARM in our case)
  With choice of compiler depending on language
3) Copy binary file to target board

## Slide 5: Goal
Create an embedded app that can communicate over a radio
  Not Wifi
  Not Bluetooth
  Custom RF signals
Create script to allow repeat:
  Builds
  Deployments
  Unit Tests

## Slide 6: Hardware
Arduino Pro 328 – 3.3V
Sparkfun RFM69 Transceiver (915 MHz)

## Slide 7: Extra Hardware
Raspberry Pi
Sparkfun RFM69 Transceiver (915 MHz)

## Slide 8: Arduino IDE
https://www.arduino.cc/
Pros
  Easy to setup
  Abstracts low level concepts
  C and C++ under the hood
  Adding external libraries is very easy
Cons
  Built for prototyping
  Proprietary project system

## Slide 9: Atmel Studio
Pros
  Lots of tools built in
  Can work with C, C++, and Arduino projects
  Familiar if you use Visual Studio
Cons
  Some manual setup
  Proprietary project system

## Slide 10: Roll Your Own with CMake
Pros
  Cross Platform
  Cross IDE
  Can add unit tests!!!
Cons
  Lots of time to setup
  Easy to lose cross-platform benefits

## Slide 11: Other Systems
Arduino CLI
  https://github.com/arduino/arduino-cli
  Arduino IDE, but a CLI tool
  Meant for scripting scenarios
IoTZ
  https://github.com/Azure/iotz
  Wrapper to other tools for working with embedded applications
    One Stop Shop for embedded tooling
  NPM Package

## Slide 12: What’s Installed on the Machine
Arduino
  Just for AVRDude. You may not need this for your projects.
Atmel Studio
  AVR Toolchain
    C/C++ compilers, linker, etc
  AVR Standard Library
  Note: Arduino IDE Installs this too
    Atmel Studio has newer versions than what Arduino comes with
Visual Studio 2017
  Include C++ features
  Include Windows 8.1 SDK (for compiling unit tests to x86)
NMake
  Installed by Visual Studio
CMake

## Slide 13: Embedded C/C++ Gotchas
No stdlib
  Missing a lot of features you’re used to
    ‘new’ keyword
  Can make your own or find them online
Trickery involved in getting unit tests created/run
Can’t debug unit tests easily
  Even though they’re compiled for x86

## Slide 14: Cmake Gotchas
Manually add/remove files included in compilation
Variable scope/lifetime

## Slide 15: What else to look into?
Debuggers
  They exist!
  No idea how they work…
Other build systems for C/C++
  https://medium.com/@julienjorge/an-overview-of-build-systems-mostly-for-c-projects-ac9931494444
Rust Language?
  Found a compiler somewhere on the internet to generate AVR. Not officially supported.

## Slide 16: Other Resources
ATMEL AVR Microcontrollers book
  Starts out with a great description embedded development in general
  https://www.amazon.com/Programming-Interfacing-ATMELs-Thomas-Grace/dp/1305509994